Gold wire electron acceleration
Work in progress of gold wire simulations in 3D using a moving window

---
Contents
- Overview of simulations
- 2D moving window simulation:
  - Setup of simulation
  - Results of 2D simulation
  - Observations
- 3D moving window simulation:
  - Setup of 3D simulation
  - Results of 3D simulation
  - Observations
- Next steps

---
Overview of simulation
Just for reminders here are some of the key features of the experiment that the simulation is trying to reproduce.
- Laser with a focal FWHM = 3.5 micron
- Target fine gold wire with width = 2.0 micron
- Target has sharp pre-plasma (see input deck).
- Polarization oriented perpendicular to long wire axis.
- Intensity 4.5 x1019 W/cm2
- Duration 30 fs with sin2 window
- Wavelength 0.8 micron

---
Contents
- Overview of simulations
- 2D moving window simulation:
  - Setup of simulation
  - Results of 2D simulation
  - Observations
- 3D moving window simulation:
  - Setup of 3D simulation
  - Results of 3D simulation
  - Observations
- Next steps

---
Initial 2D simulation
- Main parameters changed: Moving window, and B.C.
  - Moving window moves at c in positive x direction, starts at 40 fs
  - B.C. changed to simple_outflow (CPML don’t behave well with moving windows)
  - Box size increased to account for diffraction later in time.
  - Increase in particle count (4000 e, 500 Au, 500 p, per cell)
  - (Decreased density from 3000 nc to 800 nc for comparison to 3D PIC, no significant difference observable in results when this change is made in 2D (see results in shared website, I can do further comparisons to convince if needed))
- Key observations in 2D moving window (spoilers):
  - Electron dynamics continue to evolve after they have left the wire target and continue to interact with the diffracted laser pulse.
  - Velocity angle reduces over time, possibly due to increase in px, rather than a decrease in ptrans.
  - Electron energy increases somewhat over time.

---
Velocity Angle
- Metric used to infer angular distribution, velocity angle:
- Used as it is simpler to calculate and better represents angular distribution at a detector far from source, maybe?
- Distribution of electrons are calculated over the co-ordinate spaces:
  - px vs. θ
  - εk vs. θ
  - (εk being the kinetic energy.)

---
Contents
- Overview of simulations
- 2D moving window simulation:
  - Setup of simulation
  - Results of 2D simulation
  - Observations
- 3D moving window simulation:
  - Setup of 3D simulation
  - Results of 3D simulation
  - Observations
- Next steps

---
Early in time 39 fs
Electric field units V/m
Density 1/m3
Distribution offset by 3 fs due to less frequent dumps, taken at 42 fs

---
At 60 fs
Electric field units V/m
Density 1/m3

---
Much later in time 150 fs
Electric field units V/m
Density 1/m3

---
Notes on 2D moving window
- Possible 3D effects missed, though not obvious.
- Electron dynamics continue to evolve after they have left the wire target and continue to interact with the diffracted laser pulse.
- Average velocity angle appears to reduce over time for a population of electrons, possibly due to increase in px, rather than a decrease in ptrans.
- Electron energy increases somewhat over time.

---
Contents
- Overview of simulations
- 2D moving window simulation:
  - Setup of simulation
  - Results of 2D simulation
  - Observations
- 3D moving window simulation:
  - Setup of 3D simulation
  - Results of 3D simulation
  - Observations
- Next steps

---
Contents
- Overview of simulations
- 2D moving window simulation:
  - Setup of simulation
  - Results of 2D simulation
  - Observations
- 3D moving window simulation:
  - Setup of 3D simulation
  - Results of 3D simulation
  - Observations
- Next steps

---
Adjustments made for 3D simulation
- Timestep decreased and Density decreased (800 nc) to avoid numerical instability (wire explodes ahead of the laser due to not resolving plasma frequency at 3000 nc). Whole target density was simply scaled down, pre-plasma included, so pre-plasma scale length remained constant.
- Reduction in transverse resolution, and particles per cell (over all number of particles ~10x increase though)
- Reduced frequency of data dumps.

---
3D PIC key parameters:
Species	PPC	Max n_e	800 n_c
electron	100	Move Window Start	40 fs
proton	10	Intensity	4x1019 W/cm2
gold	10	dt	0.5*CFL
Fully ionised		Current Smoothing	On
gold	10	Particle Shape	3rd Spline (5th order)
Dimension	Cells	Min (micron)	Max (micron)
x	1500	-6	9
y	1200	-6	6
z	1200	-6	6

---
Contents
- Overview of simulations
- 2D moving window simulation:
  - Setup of simulation
  - Results of 2D simulation
  - Observations
- 3D moving window simulation:
  - Setup of 3D simulation
  - Results of 3D simulation
  - Observations
- Next steps

---
Changes are difficult to observe comparing 3D to 2D
I’ve taken slices in the 3D box domain to compare to the 2D case more easily. Very similar behavior is observed in 2D and 3D.
Top row shows slice in same plane as 2D simulation takes place in, e.g. taken at z=0.
Bottom row takes slice in y=0 plane so that the wire is seen length ways.

---
Early(ish) in time t=50 fs
Electric field units V/m
Density 1/m3

---
At t=60 fs
Electric field units V/m
Density 1/m3

---
At t=100 fs
Electric field units V/m
Density 1/m3

---
Contents
- Overview of simulations
- 2D moving window simulation:
  - Setup of simulation
  - Results of 2D simulation
  - Observations
- 3D moving window simulation:
  - Setup of 3D simulation
  - Results of 3D simulation
  - Observations
- Next steps

---
Further refinements needed
- Simulation domain too small:
  - Laser diffraction significant effect, so beam gets lots wider over time
  - Box edges have a clear influence on results
  - Laser reflects off boundaries slightly earlier on in simulation
  - Consequently I only trust this simulation upto around 100 fs
- Proton behavior seems unusually static, may require extra macro-particles to resolve movement. (This may not matter)

---
Contents
- Overview of simulations
- 2D moving window simulation:
  - Setup of simulation
  - Results of 2D simulation
  - Observations
- 3D moving window simulation:
  - Setup of 3D simulation
  - Results of 3D simulation
  - Observations
- Next steps

---
Next steps
- New 3D simulation:
  - Increased macro-particles for protons (x4)
  - Increased simulation domain for B.C. problems with reflections and diffraction limiting use later on in time
  - Compilation with work done calculation integrated into EPOCH
  Post-processing:
  - Correlation between electric field phase and electron trajectory
  - Work done on particles by laser field components over time
  - Nice 3D plots instead of just slices (though these are very informative).